## Slide 1: FEDERAL HIGHWAY ADMINISTRATION’S TECHNICAL ASSISTANCE ON THE AMERICANS WITH DISABILITIES ACT REQUIREMENTS TO PROVIDE CURB RAMPS THROUGH RESURFACING
  PRESENTERS:
  Candace Groudine, Director-External Civil Rights, FHWA
  James Esselman, Special Counsel, FHWA
  Robert Mooney, Pre-Construction Team Leader, FHWA
August 20 & 21, 2013

## Slide 2: FEDERAL HIGHWAY ADMINISTRATION (FHWA)
FHWA provides stewardship over the construction, maintenance and preservation of the Nation’s highways, bridges and tunnels.
FHWA also provides technical assistance to state and local agencies in an effort to improve safety, mobility, and livability, and to encourage innovation.

## Slide 3: FHWA’s Americans with Disabilities Act Program / Section 504 of the Rehabilitation Act of 1973
The primary purpose of FHWA’s Americans with Disabilities Act (ADA) / Section 504 program is to ensure that pedestrians with disabilities have the opportunity to use the transportation system in an accessible and safe manner.

## Slide 4: Accessibility Requirements Section 504 and the ADA
  Section 504 of the Rehabilitation Act of 1973 requires…..
  Recipients and sub-recipients of Federal aid,
  that are responsible for roadways and pedestrian
  facilities, do not discriminate on the basis of disability
  in any highway transportation program, activity,
  service or benefit provided to the general public.
  FHWA’s Responsibility:
  The implementation of pedestrian access requirements from
  Section 504.

## Slide 5: Americans with Disabilities Act (ADA ) of 1990
  A civil rights statute
  Prohibits discrimination against people with disabilities in all aspects of life, including transportation.
  USDOJ has designated USDOT as the federal agency responsible for overseeing and implementing ADA compliance
  FHWA’s Responsibility: The implementation of ADA pedestrian access requirements.

## Slide 6: Title II of the ADA
Applies to:
Facilities built after 1990;
Pre-existing facilities;
All public entities, such as State and local governments, even if they are not recipients of federal funding.

## Slide 7: How Did This Joint DOJ/DOT (FHWA)Technical Assistance Come About?
Joint DOJ/DOT authority to enforce Title II
ADA Directs DOJ to effectuate Title II of ADA through regulations (28 CFR Part 35)
DOJ delegated responsibility for implementing DOJ’s ADA Title II regulations to DOT for all programs, services, and regulatory activities related to transportation
Both DOJ and DOT have enforcement authority

## Slide 8: How Did This Joint DOJ/DOT (FHWA)Technical Assistance Come About?
Alterations vs. Maintenance
DOJ Regulation (28 CFR 35.151(b)): Alteration is a change that affects or could affect the usability of all or part of a facility (such as a road)
DOJ Regulation (28 CFR 35.151(i)): Altered streets, roads, and highways must contain curb ramps where there are curbs or other barriers to a pedestrian walkway (i.e., sidewalk)
DOJ Regulation does not identify specific road treatments that qualify as alterations versus treatments that qualify as maintenance

## Slide 9: How Did This Joint DOJ/DOT (FHWA)Technical Assistance Come About?
Alterations vs. Maintenance
Prior DOJ guidance stated:
  Paving, repaving, or resurfacing were generally considered alterations
  Filling a pothole was not considered to be an alteration
Prior DOJ guidance did not provide more specific examples of maintenance activities

## Slide 10: How Did This Joint DOJ/DOT (FHWA)Technical Assistance Come About?
Alterations vs. Maintenance
Prior DOT guidance from September 2006 stated
  More specific examples of alterations and maintenance
  Including distinction between structural resurfacing (alteration) and non-structural resurfacing (maintenance)
Different levels of specificity defining alterations between DOJ and DOT created:
  Confusion in application
  Inconsistency in enforcement
  Questions from stakeholders

## Slide 11: How Did This Joint DOJ/DOT (FHWA)Technical Assistance Come About?
Alterations vs. Maintenance
DOJ and DOT (FHWA) met in 2012 to 2013
  Desire to provide clarity and consistency
  Based on feedback (comments/questions) from States, local governments, disability rights advocates, citizens
  Educated by public perception of scale of road work (i.e., heavy equipment, truck numbers, crew sizes, time)

## Slide 12: How Did This Joint DOJ/DOT (FHWA)Technical Assistance Come About?
Joint Technical Assistance
Distinguishes alterations from maintenance based on the type of road treatment:
MAINTENANCE
ALTERATION
  Chip Seals Fog Seals Scrub Sealing
  Crack Filling and Sealing Joint Crack Seals Slurry Seals
  Diamond Grinding Joint repairs Spot High-Friction Treatments
  Dowel Bar Retrofit Pavement Patching Surface Sealing
  Addition of New Layer of Asphalt Mill & Fill / Mill & Overlay
  Cape Seals New Construction
  Hot In-Place Recycling Open-graded Surface Course
  Microsurfacing / Thin-Lift Overlay Rehabilitation and Reconstruction

## Slide 13: Application of Technical Assistance
  This is a single Federal policy that identifies specific pavement treatments that are alterations:
  Alterations require the installation of curb ramps
  Maintenance applications do not require curb ramps at the time of the improvement

## Slide 14: Pavement Treatment Types (Maintenance vs. Alteration)
MAINTENANCE
ALTERATION
  Addition of New Layer of Asphalt Mill & Fill / Mill & Overlay
  Cape Seals New Construction
  Hot In-Place Recycling Open-graded Surface Course
  Microsurfacing / Thin-Lift Overlay Rehabilitation and Reconstruction
  Chip Seals Fog Seals Scrub Sealing
  Crack Filling and Sealing Joint Crack Seals Slurry Seals
  Diamond Grinding Joint repairs Spot High-Friction Treatments
  Dowel Bar Retrofit Pavement Patching Surface Sealing

## Slide 15: Pavement Treatment Types (Maintenance vs. Alteration)
MAINTENANCE
ALTERATION
  Addition of New Layer of Asphalt Mill & Fill / Mill & Overlay
  Cape Seals New Construction
  Hot In-Place Recycling Open-graded Surface Course
  Microsurfacing / Thin-Lift Overlay Rehabilitation and Reconstruction
  Chip Seals Fog Seals Scrub Sealing
  Crack Filling and Sealing Joint Crack Seals Slurry Seals
  Diamond Grinding Joint repairs Spot High-Friction Treatments
  Dowel Bar Retrofit Pavement Patching Surface Sealing
plus

## Slide 16: Pavement Treatment Types (Maintenance vs. Alteration)
MAINTENANCE
ALTERATION
  Potholes
  Everything Else
  (besides potholes)
Prior to DOJ/DOT
Agreement

## Slide 17
New Project
(not yet advertised)
Maintenance
Proceed w/ Work
Alteration
Existing Sidewalks /
Prepared Surfaces w/ Barriers
No
Yes
Proceed w/Work
Meets 1991 or 2010 Standards
Yes*
Proceed w/Work
No
Install/Update Curb Ramps
*If sidewalk work is performed, then curb ramps must be updated to 2010 standards

## Slide 18: Example of Implementation
  Current Fiscal Year 2014 Plan
  Project A = Slurry Seal
  Project B = Mill & Fill
  Project C = Microsurfacing
  Project D = Reconstruction

## Slide 19: Example of Implementation
  Updated Fiscal Year 2014 Plan
  Project A = Slurry Seal
  Project B = Mill & Fill
  Project B1 = Install Curb Ramp
  Project C = Microsurfacing
  (project does not have sidewalks)
  Project D = Reconstruction (including curb ramp work)
  Current Fiscal Year 2014 Plan
  Project A = Slurry Seal
  Project B = Mill & Fill
  Project C = Microsurfacing
  Project D = Reconstruction

## Slide 20: Application of Technical Assistance
  Consistent approach among States
  Projects ready for Construction Advertisement or are under contract may proceed
  Update Pavement Preservation/Resurfacing Program
  Update any existing resurfacing ADA policies

## Slide 21: Implementing the Joint Technical Assistance: FHWA’s Expectations
  FHWA Divisions and States Provide Program Oversight by:
    Informing recipients/sub-recipients of their accessibility responsibilities
    Reviewing and monitoring pedestrian access compliance
    Reviewing the ADA transition plan …and States updating the plan as necessary

## Slide 22: Implementing the Joint Technical Assistance: FHWA’s Expectations
FHWA Divisions and States ensure:
1) Compliance of any project for construction or alteration of a facility that provides access to pedestrians
2) Incorporation of access improvements within the scope of the project that alters the use of the public rights-of-way
3) Recipients and sub-recipients apply appropriate accessibility standards to all transportation facilities.

## Slide 23
  QUESTIONS?

## Slide 24: Pavement Treatment Types (Maintenance vs. Alteration)
MAINTENANCE
ALTERATION
  Chip Seals Fog Seals Scrub Sealing
  Crack Filling and Sealing Joint Crack Seals Slurry Seals
  Diamond Grinding Joint repairs Spot High-Friction Treatments
  Dowel Bar Retrofit Pavement Patching Surface Sealing
  Addition of New Layer of Asphalt Mill & Fill / Mill & Overlay
  Cape Seals New Construction
  Hot In-Place Recycling Open-graded Surface Course
  Microsurfacing / Thin-Lift Overlay Rehabilitation and Reconstruction

## Slide 25: CONTACTS FOR QUESTIONS
  Brooke Struve, RC Safety & Design Team, FHWA,
  720-963-3270, Brooke.Struve@dot.gov
  Candace Groudine, Director-External Civil Rights, FHWA, 202-366-4634, Candace.Groudine@dot.gov
  Patrick Gomez, Civil Rights Specialist, FHWA,
  720-963-3269, Patrick.Gomez@dot.gov
  James Esselman, Special Counsel, FHWA,
  202-366-6181, James.Esselman@dot.gov
  Robert Mooney, Pre-Construction Team, FHWA,
  202-366-2221, Robert.Mooney@dot.gov